SERVICE LINE INSTALLATION STANDARDS

10’ separation between waterline and any sewer or septic system

18” separation between waterline and sewer line if crossing is necessary

3’ separation between electric lines and waterline when running parallel

LPRW crew has the right to dig an OSHA safe trench on your property

LPRW will to the best of their ability do a onetime clean up to the area disturbed at the time of installation.  Subsequent filling, leveling, or other dirt work will be the owner’s responsibility.

LPRW will not be responsible for damage done to obstructions placed over our trench after construction is complete and may refuse to perform service work on lines below or adjacent to these obstructions.

Service line valves are to remain accessible to LPRW personnel and adequately marked for easy identification.

ADDITION FOR LIVESTOCK CONFINEMENT FACILITIES

Service installation for livestock confinement facilities will be into an office area not requiring shower in to perform routine meter maintenance or into an LPRW approved metering pit at minimum distance of 100’ from the confinement structure or on the property line.  Lines will not be installed through any storage structures.

Please sign and return a copy to LPRW

______________________________

Home or Business Owner